## Slide 1
Team Members Stakeholders
Clay Hillyard Jeff Reinbolt, PhD
A.J. Kosinski Jindong Tan, PhD
Jesse Thompson
Payton McNabb
Development of an Energy-Harvesting Shoe
Department of Mechanical, Aerospace, and Biomedical Engineering, College of Engineering, The University of Tennessee, Knoxville, TN 37916
ACJP Energy
Harvesters

## Slide 2
Our goal is to convert kinetic energy into electrical energy and store it for later use to an external device
  Piezoelectric strips
  USB port
  Running shoe
  2 AAA rechargeable batteries
  Circuit board
Objective

## Slide 3
Design Functions and Requirements
Table 1. Functions and Requirements |  |  |  |  |  |  | 
Performance Requirements |  | Non-functional Requirements |  | Interface Requirements |  | Constraints | 
Requirement | Verification | Requirement | Verification | Requirement | Verification | Requirement | Verification
Battery is fully charged by a person walking 2 miles | Test | System does not cause environmental damage (pollution, etc.) | Inspection | Piezoelectric devices fit inside shoe | Inspection | System fits in a size 10 shoe | Test
Battery can fully charge an iPhone 5 | Test | Cord to battery does not trip user | Inspection | Battery is connected to shoe | Test | Battery attachment is light weight | Test
iPhone 5 cord may be plugged into battery attachment for power | Test | Battery attachment is universal for all users and shoes | Inspection |  |  | Strips and circuit board are lightweight | Test

## Slide 4
PowerSole
  Kinetic energy converted to electrical energy
    Faraday’s Law
  USB accessible
  Patent is pending
Figure 1. PowerSole uses a Faraday coil to store energy.
Research: PowerSole

## Slide 5: Research: MIT Bimorph Design
Bimorph produces more power
Forward-Switching Converter System
Roughly1.3 mW of useful power output
Figure 3. PZT Bimorph made of 2 THUNDER strips and a copper plate.
Figure 2. MIT Energy-Harvesting Shoe Design

## Slide 6: Idea from MIT Bimorph Design
Figure 4. Original idea incorporating 1)bimorph and 2)off-the-shelf energy-harvesting circuit board.

## Slide 7: Circuit Board Case from Crank Flashlight
Figure 5. Solidworks drawing image of circuit board case.

## Slide 8: Circuit Board from Crank Flashight
Figure 7. Hole for USB port.
Figure 6. Hole for wires.

## Slide 9: Working Prototype
Figure 7. Working prototype incorporating ROTHCO Weatherproof Hiking Boot

## Slide 10: Working Prototype
Figure 8. Working prototype
Figure 9. 6 Piezoelectric Strips

## Slide 11: Battery Discharge Test
Figure 10. Battery discharged by a 10 Ω resistor and data is stored on a SCOPE program
Measure actual battery capacity & energy
Reference graph to quantify performance in future tests
Rated Capacity = 1.92 W-hr
Actual Capacity = 1.21 W-hr
Rated energy in batteries = 6912 J
Actual energy in batteries = 4341.37 J

## Slide 12: Battery Discharge Test
Chart: Time (seconds)
Figure 11. 2 Duracell AAA batteries while being discharged

## Slide 13: Working Prototype: Walking Test 1
Walk on the track for 1 hour
Measure voltage before and after in discharge set-up
Use reference discharge graph to determine energy to battery
Table 2. Walking Test I Results
Number of Steps
3005
Test 1 Energy Added (J)
120.3141925
Test 1 Energy Added Per Step (J)
0.040038001
Test 1 Capacity Added (W-hr)
0.037376185
Test 1 % Charged
2.771341229
Hours to Fully Charge
36.08361142

## Slide 14: Final Product
Figure 13. Top view of final product
Figure 12. Final product with circuit board on the outside

## Slide 15: Final Product: Walking Test II
Table 3. Walking Test II Results
Number of Steps
3175
Test 1 Energy Added (J)
157.2697734
Test 1 Energy Added Per Step (J)
0.049533787
Test 1 Capacity Added (W-hr)
0.04368842
Test 1 % Charged
3.622583489
Hours to Fully Charge
27.60460879

## Slide 16: If We Started A Company
Large market of hikers and outdoor enthusiasts
  Need for charged batteries for outdoor technology
Develop our own materials to decrease production costs
  Increase product performance
Potential Stores
  Bass Pro Shop, Gander Mountain, Cabelas, etc.

## Slide 17: Obstacles Overcame
Difficulty finding good piezoelectric strips
THUNDER strips were brittle
Attaching wires to piezoelectric strips
Installing circuit board in sole of boot
  Off-the-shelf didn’t meet our needs
Lack of knowledge of power electronics circuitry

## Slide 18: Lessons Learned
Not ideal application for piezoelectric strips
  Most applications involve high frequencies
Need knowledge of power electronics circuitry for ideal results
Efficiently work as a team
  Meetings, Manufacturing, Research, etc.
Better understanding of the design process

## Slide 19: Future Work
Custom design the circuit board
Obtain data in real time
Weatherproof the design
Slimmer, more compact circuit board housing
Custom interior padding for more comfort

## Slide 20: Questions?